School of Engineering
Universidad Autonoma de Madrid (Spain)
Uni Hamburg. FB Informatik. AB TAMS. May 2006
Juan Gonzalez Gomez
Modular robotics and locomotion

---
Introduction to robotics
Introduction to modular robotics
Starting platform: Y1 Modules
Locomotion of minimal configurations
Locomotion of 1D worm-like robot
Locomotion of 2D snake-like robots
Future work
Contents

---
Introduction to
robotics

---
Main areas of robotics
Locomotion: Capability of the robots to move from one point to another
Manipulation: Robots that are able to grasp and manipulate objects
Industrial robots
Service Robots
Mobile robots

---
Locomotion: Classification of mobile robots (I)
Mobile robots can be classified according to environment in which they move:
Air. Flying robots: robotics planes, helicopters, insects...
Water. Swimming robots: fish, snakes
Earth. Terrestrial robots: Move on a surface
Horizontal surface: Locomotion on the ground
Vertical surface: Climbing robots.

---
Locomotion: Classification of mobile robots (II)
Mobile robots can be classified according to the elements used to perform the locomotion:
Wheeled robots
tracked robots
Legged robots
Body-motion robots

---
Wheeled robots
Locomotion is easy to achieve
They are very efficient
Mechanics is very well known
DISADVANTAGE:
They can only move on special surfaces

---
Tracked robots
Very similar to wheeled robot
They can move better in a rough terrain

---
Legged robots
Higher power consumption
More complex
Coordination problem
2 legs
Why there are so many legged animals in the nature?
8 legs
6 legs
4 legs

---
Body-motion robots
The locomotion is based on the movements of the body
Examples: snakes, worms...

---
Classification according the structure
Specific design
Modular design
Video
Modular approach
 Specific design of an Humanoid

---
Modular robotics

---
Introduction to
Modular Robotics (I)
Main idea: Building robots composed of modules
The design is focused in the module, not in a particular robot
The different combinations of modules are called configurations
There are two kinds of modular robots:
Manually reconfigurable robots
Self-reconfigurable robots

---
Introduction to
Modular Robotics (II)
The idea of modular robotics was introduced by Mark Yim, in 1994
There are many groups working on this topic in the world.
The most avanced robots are:
POLYBOT (USA). Palo Alto Research Center (PARC)
M-TRAN (JAPAN). Advance Industrial Science Technology (AIST)
YAMOR (Swiss). Ecole Polytechnique Federale de Lausanne (EPFL)

---
Introduction to
Modular Robotics (V)
YAMOR
The modules have 1 DOF
Manually reconfigurable
Control: ARM and FPGA
Communication via bluetooth
Connection using velcro

---
Introduction to
Modular Robotics (III)
Generation 1
POLYBOT
Manually reconfigurable
Many versions
All the modules have 1 DOF
3 generations of modules
5x5x5cm
Maxon motor
Similar electronics than G2
Generation 3
Generation 2
11x7x6 cm
Power PC 555
1MB Ram
Can Bus
Infrared emitters and detectors

---
Introduction to
Modular Robotics (IV)
M-TRAN
4 Legged
All the modules have 2 DOF
6x12x6 cm
CPU: 1 Neuron Chip and 3 PICs
Acceleration sensor
Wheel
Snake
Video

---
Starting platform:
Y1 Modules

---
Y1 Modules:
Introduction
We needed a cheap and easy-to-build platform to research on modular robotics
It was not possible to buy the modules developed by the other groups
Y1 Modules is the first generation
Fast prototyping
Manually reconfigurable robots
Students can build them very easily

---
Y1 module:
Characteristics
Material: 3mm Plastic
Servo: Futaba 3003
Dimension: 52x52x72mm
Range: 180 degrees
Two types of connection:
90 degrees rotation
Same orientation
Video

---
Y1 modules:
Building in 6 steps

---
Y1 modules:
Topology
 1D: Chain robots
 (Worms, snakes)
 2D structures
 3D structures

---
Y1 Modules:
1D Structures (Chain robots)
Two different type of robots:
Same orientation
90 degrees rotation

---
Y1 modules:
Electronics
The electronic and power supply are located outside the module
An 8 bits micro-controller is used for the generation of the PWM signal that position the servos
The software running in the PC send the position to the servos by serial communication
Y1 Modules
RS-232
PWM
PC
Power supply

---
Y1 modules:
Software
The modules are controlled by the PC
The software can set the position of every module
There is an simple API
Application
Position each module
Enable/disable each module
API
Modules
controller
Demo
Let's see some code...
Let's move one module...

---
Locomotion of minimal configurations

---
Introduction
Complex robots can be constructed by attaching these modules
But, what we wonder is:
How do these modules have to be coordinated to achieve the locomotion?
What is the minimum number of modules needed to achieve locomotion in 1D and 2D?

---
Configuration with one module (II)
Can one module move from one point to another??
How can we test it?
????
Test
Let's move one module...

---
Configuration with one module
Answer: no locomotion
Let's try with two modules...

---
Configuration with two modules:
Pitch-Pitch
Pitch axis
Can this robot move from one point to another?
if so ... How do we have to coordinate the articulations?
Test
????
Let's move two modules...

---
Configuration with two modules:
Pitch-Pitch
Pitch axis
Answer: yes!!
only two modules is enough for locomotion in 1D
The robot can move forward and backward
Let's try to study what happened...

---
Configuration Pitch-Pitch:
Coordination
1
2
p
2
j
=
Asin(
t)
1
T
p
2
Df
t+
j
=
Asin(
)
2
T
Two sinusoidal waves are applied to each articulation
These waves only differ on the phase ( )
determines the coordination of the movement
Df
Df

---
Configuration I (Pitch-Pitch)
Results
5,5
5
Df
When is in the range [100, 130] degrees, the speed is maximum and the coordination is the best.
4,5
4
3,5
3
2,5
2
Demo
1,5
1
0,5
0
0
25
50
75
100
125
150
175
200
Df
ΔS (cm/cycle)

---
Locomotion in 2D
Now we want to build the minimal configuration capable of moving in 2D
How many modules are necessary?
What is the coordination?
One module is not enough...
Two modules?
Three modules?
????

---
Locomotion in 2D
Let's try this configuration...
Can this robot move from one point to another?
Test
Let's move two modules...

---
Locomotion in 2D
ANSWER: NO
Let's try with three modules...
How can we connect the modules?
Are three modules enough for moving in 2D?
How are the modules coordinates?
Test
Let's move three modules...

---
Configuration II (Pitch-Yaw-Pitch)
Description
Yaw Axis
1
2
3
Pitch axis
Pitch axis
Three modules: two rotating in the pitch axis and one in the yaw
We call it Pitch-Yaw-Pitch configuration (PYP)
1D and 2D sinusoidal gait
Lateral shift gait
Lateral rolling gait

---
Configuration II (Pitch-Yaw-Pitch)
1D sinusoidal gait
1
2
3
p
2
j
=
Asin(
t)
1
T
p
2
Df
t +
j
=
Asin(
)
3
T
The angle of articulation 2 fixed to 0 degrees
Articulations 1 and 3 coordinated in the same way that in the PP configuration
Sames results as in configuration PP
j
2
0
=

---
Configuration II (Pitch-Yaw-Pitch)
2D sinusoidal gait
1
2
3
p
2
j
=
Asin(
t)
1
T
p
2
Df
t +
j
=
Asin(
)
3
T
The same as in 1D sinusoidal gait, but the angle of articulation 2 different from 0 degrees
The trajectory of the robot is an arc
j
2
0
=

---
Configuration II (Pitch-Yaw-Pitch)
Lateral shift gait
1
2
3
p
2
j
=
Asin(
t)
1
T
p
2
t +
j
=
Asin(
)
2
T
A<=40
Module 1 and 3 are in phase
Module 2 is 90 degrees out of phase
The robot moves parallel to its body axis
j
3
=
j
1
p
2

---
Configuration II (Pitch-Yaw-Pitch)
Lateral rolling gait
The same coordination as in the lateral shift gait, but using and amplitude A>60 degrees.
The sense of rolling can also be controlled by changing the sign of the difference of phase
The robot rolls about its body axis

---
Minimal configuration in 2D
At least, we need three modules...
????
Test
Which is the minimal configuration in 2D that can move from one point to another?
How do we have to coordinate the modules?

---
Configuration III: three-modules star
Description
1
2
3
Three modules in the same plane, moving about its pitch axis
The angle between the modules is 120 degrees (connected in a three-points-star form)
1D sinusoidal gait along six different directions
Rotation about the robot's yaw axis

---
Configuration III: three-modules star
1D sinusoidal gait
1
3
2
The robot can move along six different directions
Three sinusoidal waves are applied
Example: In order to move along the red direction:
=
=
Df
<130
100<
j
2
j
3
Asin(
2
p
T
)
j
1
Df
Asin(
2
p
T
+
)
Df
Asin(
2
p
T
+
)
=

---
Configuration III: three-modules star
Rotation about its yaw axis
1
3
2
Rotation about the robot yaw axis
Three sinusoidal waves are applied
Video
j
1
Asin(
2
p
T
Asin(
2
p
T
)
=
j
2
Asin(
2
p
T
Asin(
2
p
)
=
2
p
3
2
p
+
j
3
Asin(
2
p
T
Asin(
2
p
)
=
4
p
3
p
+

---
Conclusions...
We have found three minimal configurations:
2D Structure
1D Structure
1D Structure
Locomotion in 2D
Locomotion in 1D
Locomotion in 2D
Rotating
Rolling
All of these robots are controlled using sinusoidal signals
The phase difference determines the coordination between the modules
A: Amplitude
p
2
T: Period
f
j
=
Asin(
t+
)
f
T
: Phase

---
Conclusions...
We have discover the basic coordination method that is found in nature.
All the vertebrates have central pattern generators (CPGs) in the Cord.
CPG are oscillators that generate periodic signals that are applied to the muscles, making the animal move.
CPGs
Cord

---
Conclusions...
We are applying the same model that in nature, but a little simplied
p
2
f
j
=
Asin(
t+
)
CPG
T
There are one CPG per module:
Module 1
Module 2
Module 3
Module 4
CPG
CPG
CPG
CPG

---
Conclusions...
We have found a general control method valid for all the configurations!!!
We only have to find the different parameters of the CPG: Phase difference, Amplitude and period.

---
Locomotion of 1D worm-like robot

---
1D chain robot:
Introduction
Configuration: 8 Y1 modules in the same orientation
Dimensions: 52x52x576mm:

---
1D Chain robot:
Locomotion approaches
Two approaches can be used for the locomotion:
Using 8 CPGs
Using a global wave that travel through the robot, from the tail to the head
For the second approach only 4 parameters have to be specified:
Waveform
Wavelength
Amplitude
Period

---
1D chain robots:
Global waves
The locomotion characteristics depend on the global wave used:
High amplitude: Crossing over obstacles
Low amplitude: Going inside a tube
Semi-sine wave: Caterpillar locomotion

---
1D chain robots:
Locomotion capabilities
One feature of these robots is that they can change their shape:
Video

---
Locomotion of 2D snake-robot

---
Chain robot 2D:
Introduction
Robot composed of 8 Y1 modules
Two adjacent modules are 90 degrees rotated
90 degrees rotation
This robot have the following locomotion capabilities:
1D locomotion
1D locomotion in an arc
Lateral shift
Rotating parallel to the ground
Lateral rolling

---
Chain robot 2D:
Control approaches
Using 8 CPGs
Using two global waves. One for the vertical modules and the other for the horizontal:
Some gaits are easier to implement with the first approach and others with the second

---
Chain robot 2D:
1D locomotion
Locomotion in 1D: straight and arc trajectories
Df=120
Fixed: 0 degrees
Fixed: 30 degrees
CPG
CPG
CPG
CPG
CPG
CPG
CPG
CPG

---
Chain robot 2D:
2D locomotion
Locomotion in 2D: Lateral shift and rotating
Df=90
Shift right
Horizontal wave
Df=-90
Shift left
Df=0
Anti-clockwise
rotation
Df=180
Clockwise
rotation
Vertical wave

---
Chain robot 2D:
Lateral rolling
Two CPGs are used for vertical and horizontal modules
The phase difference between them is 90 degrees
The robot rotates about its body axis
Df=90
Demo
CPG
CPG

---
Future work (I)
We are designing a new module (GZ2)
The servo is more powerful
It is stronger: made of aluminium
It has four connection plates

---
Future work (II)
Caterpillar configuration:
Snake configuration:

---
Future work
4 Leg configuration

---
Future work
Humanoid configuration

---
School of Engineering
Universidad Autonoma de Madrid (Spain)
Uni Hamburg. FB Informatik. AB TAMS. April 2006
Juan Gonzalez Gomez
Modular robotics and locomotion